## Slide 1: Ch.13 Source Rock Evaluation
Source Rock Definitions
  Source rock: A unit of rock within which sufficient hydrocarbons have been generated, and from which sufficient hydrocarbons have migrated to forma a commercial accumulation of oil or gas.
  Possible source rock: Generally, for any given rock, geochemical source rock analysis do not yield information which can be used to tell if hydrocarbons actually have migrated from that rock. From an operational standpoint, then, every rock is a possible source rock.
  Active source bed: A unit of rock that is in the process of generating and expelling oil or gas
  Potential source rock: A unit of rock that has the capacity to generate oil or gas in sufficient quantities to form commercial accumulations, but has not yet done so because of insufficient thermal maturation.
  Limited source bed: A unit of rock that does not contain enough volume to source commercial accumulations. Examples are thin shale laminations in carbonates and thin coal stringers in various strata.
  Quiescent potential source bed: A source bed that was once active but has temporaily stopped generating and expelling hydrocarbons. Such situations are usually assciated with thermal cooling due to uplift and erosion. An uplifted formation may still have source potential if reburied.
  Spent source bed: A source bed that has completed the process of oil or gas heneration and expulsion. It may be spent for oil but active for gas

## Slide 2
Source Rock Characterization with Pyrolysis
  Pyrolysis 장점
    빠른 분석 (~30min)
    저렴한 비용
    쉬운 이동 (휴대 가능)
    적은 시료의 양 (~100mg)

## Slide 3
http://wiki.aapg.org/Rock-Eval_pyrolysis

## Slide 4
Peak | Is a measurement of… | Comment
S1 mg Hc/g rock | The free hydrocarbons present in the sample before the analysis | Can be thought of as a residual hydrocarbon phase. When S1 is large relative to S2, an alternative source such as migrated hydrocarbons or contamination should be suspected
S2 mg Hc/g rock | The volume of hydrocarbons that formed during thermal pyrolysis of the sample | Used to estimate the remaining hydrocarbon generating potential of the sample
S3 mg Co2/g rock | The CO2 yield during thermal breakdown of kerogen | Most prevalent in calcareous source rocks.
S4 mg carbon/g rock | The residual carbon content of the sample | Residual carbon content of sample has little or no potential to generate hydrocarbons due to a lack of hydrogen and the chemical structure of the molecule
%TOC=[0.082(S1+S2)+S4]/10
http://wiki.aapg.org/Rock-Eval_pyrolysis

## Slide 5
Pyrolysis로부터
  석유 발생 잠재성 (oil generation potential)
  유기물 유형 (organic matter type)
  열적 성숙도 ( thermal maturity)

## Slide 6
S1 +S2 (ppm) | 0-2 | 2-6 | 6-20 | 20-60{-100+ (oil shale)}
Source rock potential | poor | fair | good | Very good
Type of product | Gas, light oil | Oil & gas Various proportion |  | 
Geologic examples | Duala Basin, Gulf coast Tertiary sed., Pierre sh., Mancos | Phosphoria, Mowry sh., Niobrora | Phosphoria, Toartian sh., Paris Tertiary | Green river, Bakken/ Exshad, Minnolusa, Cretaceous Persian Gulf Coast
석유 발생 잠재성
  S1+S2의 양(kg/ton, mg/g, ppm)에 따라

## Slide 7
유기물의 유형 (Type of Kerogen)
  S2/TOC= hydrogen index can be converted to H/C
  S3/TOC= oxygen index can be converted to O/C
  S2/S3 = H/O, 높을수록 잠재성 떨어짐 (예, type III)

## Slide 8
Figure 7 Modified Van Krevelen diagram of the hydrogen index (HI) vs. the oxygen index (OI). Little to no remaining hydrocarbon generation potential is indicated for the samples. The enlarged section (right) displays the highest HI and OI values for the Upper Devonian sample 119.628 from the Arkhangel Bay, suggesting slightly lower maturities toward the north of Novaya Zemlya. TOC = total organic carbon.
http://aapgbull.geoscienceworld.org/cgi/content-nw/full/94/6/791/FG7

## Slide 9
http://www.chemterra.com/resource-play-consulting/

## Slide 10
열적 성숙도
  HI vs OI Van Krevelen diagram 상의 위치
  S2 peak의 위치
  Production index or transformation ratio = S2/(S3+S3) 값

## Slide 11
Stage of Thermal Maturity | Temperature | Process | Product
Immature | <60 o C | Bacterial and plant organic matter converted to kerogens and bitumen | Methane generated by microbial activity
Mature | 60 o C -160 o C | Rock generates and expels most of it's oil | Oil
Postmature | >160 o C | Postmature for oil/mature for gas | Gas
http://www.dcnr.state.pa.us/topogeo/econresource/oilandgas/marcellus/sourcerock_index/sourcerock_maturation/index.htm

## Slide 13
Crossplots of HI vs Tmax and HI vs Ro determine organic maturity, kerogen type, and whether the rock is in the oil or gas window. Immature and post mature rocks are not overly interesting as possible source or reservoir rocks.
https://spec2000.net/11-vshtoc.htm

## Slide 14
Fig. 8: Plot of PI versus Tmax of the lignite samples from Ogwashi-Asaba Formation
http://scialert.net/fulltext/?doi=ajes.2011.157.170

## Slide 15
Pyrolysis 해석 상 문제점
  Tmax decreases as sample weight increases
  Tmax increases as grain size increases
  Flow rate: too slow  saturate the dectector and slow the response
  Splitter tempertaure too high  may see extra peak (due to ionization)
  Too heavy or too lean samples may cause some errors in Tmax determination
  Mineral matrix effect
  Flame ionization detector error